## Slide 1: Digital Communications: Error Correction Codes for Wireless Communication Systems
Sami Khorbotly, Ph.D., IEEE member
Assistant Professor
Dept. of Elec. & Comp. Eng. & Comp. Sc.
Ohio Northern University

## Slide 2: Wireless Communications
TV & radio
broadcasting
Cell phones
Wireless internet
911 services
Transportations
Geolocation/GPS
Military/Battlefield
Law enforcement

## Slide 3: Types of Transmitted Data
Transmitter
Receiver
Image/video
Files/data
Text messages
Speech/music
Files/data
Speech/music
Image/video & text

## Slide 4: Sample Communication System (Image)
Source Encoder
Source Decoder
Binary signal
…100101…
Transmitter
Modulated binary signal
…110100…
Receiver
Binary signal
…100101…

## Slide 5: Noise, Interference & other issues
Unfortunate, error causing effects in the wireless communication channel :
Multi-path propagation of the signal
Interference from other communication devices

## Slide 6: How does error occur?
1 0 0 1 1 0 1 0 1 0 0 0 1 0 1 1 1 0 1 0
1 0 1 1 0 1 0 0 1 . . .
Transmitted data bits
Transmitted waveform
Received waveform
Received data bits

## Slide 7: Text Message Example
Source Encoder
Source Decoder
…1001010
1010011100010010010110010…
Transmitter
Receiver
Fire at 100 Main St.
Noise &
interference
…1011010
1011011000010100010100010…
Fore as 140 Vain St@

## Slide 8: Society Without Reliable Comm.
Cell Phones
Hard to hold a meaningful conversation (voice)
TV & Radio Broadcasting
The corrupted image/Music will turn the audience away
Wireless internet
Corrupted emails
Credit card purchases not going through
Surfing the net is so annoying it is not even worth it
Geolocation/GPS
Good luck getting to your destination

## Slide 9: Society Without Reliable Comm.(Cont)
911 Services
Paramedics/fire fighters going to the wrong address; potential loss of lives and property
Transportations
Airplanes simultaneously landing on the same runway
Boats colliding across the oceans
Law Enforcement
Officers unable to call for backup
Military/Battlefield
Combat units moving/firing in the wrong direction

## Slide 10: What Can We Do?
Who cares about wireless communications? Let’s wire every thing up.
Come up with a way to reduce error the error in the received signal.
Error Correction Coding
Also known as
Channel Coding

## Slide 11: Channel Encoding
Additional blocks
Channel encoder at the transmitter side
Channel decoder at the receiver side
Source Encoder
Source Decoder
Transmitter
Receiver
Channel Encoder
Channel Decoder

## Slide 12: Error Correction Coding
Channel encoder: Manipulates the source data in such a way to reduce the probability of error in the received signal
Channel decoder: At the receiver side, designed in coordination with the encoder to recover the source data
Infinite possibilities and designs of encoder/decoder pairs
The probability of error can be significantly reduced at the expense of a lower transmission rate

## Slide 13: Redundancy Coding
In n-redundancy coding, each data bit is encoded in n bits.
For example, in a 3-redundancy coding scheme, a ‘0’ data bit is encoded as ‘000’ and a ‘1’ data bit is encoded as ‘111’.
The channel decoder generates a data bit out of a block of n bits. (3 in the example)
Channel Encoder
Channel Decoder
100
100
111000000
111000000

## Slide 14: How does it reduce the error?
The decoder is taking blocks of n bits. (n=3 in the example)
The decoder expects all n bits to have the same value
When the n bits in a block do not have the same value, the decoder detects an error
Some of the errors can be corrected
Channel Decoder
000
0
001
0
111
1
101
1

## Slide 15: Signal Transmission Example
001011
000|000|111|000|111|111
010|001|100|100|011|011
Channel Encoder
Channel Decoder
6 data bits
18 encoded bits
(3 redundancy)
7/18 received bits are erroneous
1/6 decoded bits are erroneous
000011
Error reduced from 7/18 bits (38.89%) to 1/6 bits (16.67%)
Notice the one data bit still received in error

## Slide 16: Correction Abilities of Codes
Assuming a ‘0’ data bit is transmitted:
Received | 000 |  | 010 |  | 100 | 101 |  | 111
Decoded | 0 |  | 0 |  | 0 | 1 |  | 1
In a 3-redundancy coding, the transmitted coded word is ‘000’
In a 5-redundancy coding, the transmitted coded word is ‘00000’
Received | 00000 |  | 00010 |  | 01001 | 01011 |  | 10111
Decoded | 0 |  | 0 |  | 0 | 1 |  | 1
3-redundancy coding can correct 1 error bit in a coded word
5 redundancy coding can correct up to 2 error bits in a coded word

## Slide 17: Correction Abilities of Codes (cont.)
General formula:
n-redundancy coding can correct up to (n-1)/2 bits in a code
The larger the value of n, the higher is the correction ability
Why do we not use a really large value for n, let’s say a
1,000,000 redundancy encoder?

## Slide 18: Time Performance Trade-off
Assume a communication system operating at a rate of 100 kilo bits per second (kbps)
If the data to be transmitted is 10 kilo bits, the non-coded signal will be transmitted in 10/100=0.1 sec
The encoded signal containing more bits will take longer:
n
Time (sec)
1
2
5
10
100
0.1
0.2
0.5
1
10

## Slide 19: Trade-off decision
If the delay in the original (non-coded) system is 1 ms
The original system results in 30% bit error rate (BER)
Are you willing to use an encoding that reduces the BER to 5 % at the expense of increasing the delay to 10 ms?
How about an encoding that reduces the BER to 0.2 % at the expense of increasing the delay to 2 s?
Time delay between parties

## Slide 20: Delay Sensitivity
Different application can afford different levels of delay
A 30 seconds delay is affordable when sending an email or downloading a file
A 30 seconds delay between talking parties is unacceptable. Especially if law enforcement or emergency situations are involved
Design engineers make their decision based on the sensitivity and nature of their application

## Slide 21: Convolutional Coding
Also reduces the error in communication systems
Can achieve higher error correction at a relatively lower cost, compared to n-redundancy coding
A m/n convolutional encoder is a sequential system that generates an n bit codeword out of m data bits
The coded signal is generated by generator polynomials and modulo-2 adders.
A | B | A B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth table of a Modulo-2 adder

## Slide 22: Convolutional Coder Example
In a 1/3 encoder with generator polynomials:
G1 = (1,0,1), G2 = (0,1,1), & G3 = (1,1,0).
For each data bit x(i) corresponds a 3-bit code y1(i)y2(i)y3(i) with:
x(i), x(i-1), and x(i-2) denote the present, previous and 2 sample delayed inputs.
It is assumed that the system is originally reset to ‘0’

## Slide 23
x(i-1), x(i-2) are originally set to 0,0
if the data bit x(i)=0, the output is y=000
if the data bit x(i)=1, the output is y=101
For the second bit:
if the first bit was a 1, x(i-1), x(i-2) are 1,0
if the second data bit x(i)=0, the output is y=011
if the second data bit x(i)=1, the output is y=110
if the first bit was a 0, x(i-1), x(i-2) are still 0,0
if the second data bit x(i)=0, the output is y=000
if the second data bit x(i)=1, the output is y=101
This approach can be adopted to build a tree diagram
Example (cont.)

## Slide 24
x(i,i-1,i-2):000
Output: N/A
x(i,i-1,i-2):000
Output:000
x(i,i-1,i-2):000
Output:000
x(i,i-1,i-2):100
Output:101
x(i,i-1,i-2):100
Output:101
x(i,i-1,i-2):010
Output:011
x(i,i-1,i-2):110
Output:110
x(i,i-1,i-2):000
Output:000
x(i,i-1,i-2):100
Output:101
x(i,i-1,i-2):010
Output:011
x(i,i-1,i-2):110
Output:110
x(i,i-1,i-2):001
Output:110
x(i,i-1,i-2):101
Output:011
x(i,i-1,i-2):011
Output:101
x(i,i-1,i-2):111
Output:000
X(i)=0
X(i)=0
X(i)=0
X(i)=0
X(i)=0
X(i)=0
X(i)=0
X(i)=1
X(i)=1
X(i)=1
X(i)=1
X(i)=1
X(i)=1
X(i)=1

## Slide 25: Example (Cont.)
Since each codeword is made of 3 data bits, x(i,i-1,i-2), the decoder reads the code words corresponding to 3 data bits
The codes corresponding to 3 data bits are 9 coded bits
According to the tree, there are only 8 valid sequences
Valid code sequences | mismatch
000 000 000 | 5
000 000 101 | 7
000 101 011 | 5
000 101 110 | 5
101 011 110 | 5
101 011 011 | 5
101 110 101 | 5
101 110 000 | 3
Received code sequence:
110 110 010
Minimum
mismatch

## Slide 26: Convolutional Coder Design
For each encoder corresponds a different tree diagram
Different coding rates & different generator polynomials result in different error correction performances
A convolutional coder with 2 or more valid code sequences that are separated by one bit is a poor coder
A better convolutional coder is where the valid code sequences are significantly separated/different from each other

## Slide 27: Valid Code Sequence Separations
Valid code sequences
000 000 000
000 000 101
000 101 011
000 101 110
101 011 110
101 011 011
101 110 101
101 110 000
2
4
2
4
2
4
2
4
6
etc

## Slide 28: Important Definitions
Modeling
Finding the mathematical equations that describe the behavior of a physical system
Computer simulation
Using the mathematical models to imitate the functionality of a real process. Commonly used to compare the performance of alternative designs before implementation
Matlab
A numerical computing and programming environment. Popularly used to perform computer simulations

## Slide 29: Computer Simulation
Transmitter
Receiver
Simulation blocks supplied by the instructor:
Image to binary converter
Transmitter
Wireless channel
Receiver
Binary to image converter
Blocks expected from you:
Encoder
Decoder

## Slide 30: Real-life System
Simulation blocks supplied by the instructor:
Image to binary converter
Transmitter Interface
Receiver Interface
Binary to image converter
Blocks expected from you:
Encoder
Decoder
The Transmitter, Receiver, and channel in this system are all real and not simulated

## Slide 31: Project
Get familiar with the Matlab environment
Take a look at the supplied simulation blocks to get familiar with Matlab programming language (very similar to C)
Write two Matlab codes to simulate respectively an encoder and a decoder using the n-redundancy scheme.
Run the simulation for various values of n to observe its effect on the performance of the system and the transmission time.

## Slide 32: Project (cont.)
Create a plot of the BER performance versus the coding rate n
Create another plot of the processing time versus the coding rate n
Create convolutional coding system. Find the BER and the processing times corresponding to your system

## Slide 33
Questions ?